THE UNIVERSITY OF IOWA

DESIGN STANDARDS & PROCEDURES

September 2023 EDITION

PREFERMENT 03

UIHC Outlets

EFFECTIVE DATE:  October 27, 2023

The information contained in this Preferment modifies, supplements, or replaces information contained in The University of Iowa Design Standards & Procedures.

APPLICABLE SECTION:	Section III – General Design Standards and Outline Specifications and Details

ATTACHMENT(S):	NONE

APPLICABLE TO SECTION III – General Design Standards and Outline Specifications and Details:

ITEM #1	Subsection 2) Space Guidelines

Article 9. University Classrooms

ADD the following articles

9.4.	Classroom Types:

9.4.1.	Seminar Room:

9.4.1.1.	Furnish with a large central table or multiple small tables that can be grouped into one (1) central table.

9.4.1.2.	Furnish with moveable tables and chairs or tablet armchairs on casters.

9.4.1.3.	Design for up to twenty-two (22) students.

9.4.1.4.	Basis of design is 25-square foot per seat.

9.4.2.	Small Classroom:

9.4.2.1.	Flat floor.

9.4.2.2.	Furnish with moveable tables and chairs.

9.4.2.3.	Design for up to fifty (50) students.

9.4.2.4.	Basis of design is 25-square foot per seat.

9.4.2.5.	When tablet armchairs are authorized, allow 18-square foot per seat.

9.4.3.	Large Classroom:

9.4.3.1.	Entrances may be located at the front of the room for disability access.

9.4.3.2.	Tiered floor or furnish with active learning furnishings environment to improve sight lines approved by Classroom Scheduling.

9.4.3.3.	Furnish with fixed tables and moveable chairs.

9.4.3.4.	Design for fifty-one (51) to ninety-nine (99) students.

9.4.3.5.	Basis of design is 20-square foot per seat.

9.4.4.	Lecture Hall/Auditoria:

9.4.4.1.	Sloped or tiered floor.

9.4.4.2.	Furnish with low maintenance, fixed tablet armchairs or table and chairs.  Fixed seats shall be labeled with row and number.

9.4.4.3.	Design for one hundred (100) or more students.

9.4.4.4.	Basis of design is 12-square feet per seat.

9.4.4.5.	Design to include lobby or gathering area adjacent to space for circulation and seating.

9.4.5.	TILE (Transform, Interact, Learn, Engage) Inquiry-Based Learning Space:

9.4.5.1.	Flat floor.

9.4.5.2.	Furnish with tables and moveable chairs.

9.4.5.3.	Spaces shall be designed creatively with primary focus on student and instructor collaboration.

9.4.6.	Shared Informal Study Space:

9.4.6.1.	These spaces are defined as individual and collaborative. Individual study is available on an unscheduled basis.

9.4.6.2.	Collaborative study space is centrally scheduled initially and thereafter on an unscheduled basis for the remaining hours.

9.4.6.3.	Furnish with equipment and infrastructure to support individual and group work.

9.4.6.4.	Provide pathway to telecommunication closet for room scheduler device at study space entrance door.

9.4.6.5.	Schedulers should be powered over Ethernet.  Consultation with ITS-LST Group for location.

END OF PREFERMENT